## Slide 1
Multi-UAV AI Framework for Disaster Response
Progress Report · MSc dissertation (LSBU) · Simulation-based
Coordinating a team of drones to search a flooded disaster area efficiently — and guide rescue.
HOW IT WORKS
1
See YOLO detects survivors, vehicles, flood water, blocked roads
2
Divide Split the area into workload-balanced drone sectors
3
Adapt Auction re-tasks drones when one fails or a survivor is found
4
Predict Forecast where a flood survivor drifts (SAROPS-style)
5
Route Safe rescue paths that avoid blocked / flooded roads
STATUS
• 8 of 9 core phases complete (perception → drift)
• 74 automated tests passing · reproducible (seeded)
• Data: VisDrone, SARD, RescueNet, FloodNet (post-hurricane flooding)
• Two YOLO11 models: detection + segmentation
• Perception & coordination decoupled — real data + CPU Monte-Carlo
• Remaining: hazard-aware routing (Phase 8) + write-up

## Slide 2
Results & Contribution
0.674
mAP@50 — survivor & vehicle detection (Model A)
+25.5 pts
coverage vs static partitioning (two UAV failures)
1,800
Monte-Carlo runs · reported mean ± 95% CI
Area coverage under UAV failure (6 UAVs)
Chart: 
| No failure | One fails | Two fail
Adaptive auction | 100 | 100 | 100
Static partition | 100 | 87.6 | 74.5
The contribution
Adaptive auction reallocation (Contract Net) beats static partitioning under failure — proven over 1,800 seeds with confidence intervals.
The novelty
Survivor-drift prediction adapted from maritime SAR (SAROPS) → drift-driven UAV re-tasking. Perception → prediction → coordination in one loop.
What's next
Hazard-weighted rescue routing (Phase 8, distance-vs-safety) · wire drift into the auction · dissertation write-up.